## Slide 1: Team Details
Case Study No. 5
VehicleGPT Edge - On-Device SLM/LLM Vehicle Assistant
Team Name: <enter team name>
Members: <names and roll numbers>
College: <college name> | Email: <contact>

## Slide 2
THE CHALLENGE
Software-defined vehicles produce answers no one can ask for
Real questions owners and service engineers ask today
“Why has my driving range reduced over the last two weeks?”
“When did fuel efficiency show the largest drop?”
“Show all ADAS disengagement events from yesterday.”
“What happened before the battery overheating warning?”
“Compare energy consumption between city and highway driving.”
Data at the source: CAN / CAN-FD · SOME/IP · Android Vehicle HAL · QNX services & logs · ADAS · camera feeds · diagnostic logs
Today: dealer visit, dongle + laptop, or a cloud portal → days. Target: the same answer, in-vehicle, in under 2 seconds.
HARD CONSTRAINTS FROM THE CASE BRIEF
No cloud dependency
local-only inference, storage and search
~2 GB RAM, ~2 ARM cores
embedded-class hardware (Pi 4/5, automotive ARM, QEMU/Graviton)
Response < 2 seconds
for common natural-language queries
Weeks of history, searchable
at least several weeks retained on-device
Safety isolation
safety-critical functions stay outside the AI system
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
1 / 10

## Slide 3
OUR SOLUTION · VEHICLEGPT EDGE
Evidence-first assistant: the model explains, the data proves
1 · SENSE & STORE
Normalisers for CAN/CAN-FD, SOME/IP, Android Vehicle HAL, QNX logs and ADAS events
One canonical time-series + event store: weeks of history on the vehicle
CARLA drives and recorded-log replay make every scenario repeatable
2 · ASK & PROVE
Local SLM (≤1.5B, 4-bit) interprets the question — it never invents the numbers
SQL, temporal and anomaly engines build an evidence package per query
Validator re-checks every figure and citation before anything is shown
3 · EXPLAIN & ACT
Plain-language answer + trend chart on head unit or service tablet
Exact lookups take a model-free fast path (typically < 200 ms)
Read-only by design: no write path to actuators or safety functions
Who it serves: Driver · Service engineer · Fleet operator · Validation & QA team
100% local: no cloud calls, no telemetry egress — works in tunnels, workshops and test yards. Response, privacy and availability do not depend on connectivity.
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
2 / 10

## Slide 4
EXPECTED OUTPUT 1 · HIGH-LEVEL SYSTEM ARCHITECTURE
Hardware and software components, integrated end-to-end
HARDWARE
Automotive ARM SBC or Raspberry Pi 5 + AI HAT · 2–8 GB RAM · NVMe/eMMC
OS & SAFETY
Linux or QNX · hypervisor-isolated AI partition · read-only bus taps
RUNTIME
llama.cpp (4-bit GGUF) · DuckDB + SQLite · containerised services
INTERFACES
SocketCAN · vsomeip · Vehicle HAL AIDL · ROS 2 / CARLA simulation
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
3 / 10

## Slide 5
EXPECTED OUTPUT 2 · VEHICLE DATA COLLECTION STRATEGY
Capture → normalise → tag → retain, every source maturity-tagged
CAPTURE
NORMALISE
TAG
STORE
SocketCAN / vsomeip / AIDL / logd
Source | Collection interface | Maturity
CAN / CAN-FD | SocketCAN + DBC decoding at 500 kbps | protocol
SOME/IP services | vsomeip listener + ARXML schema | protocol
Android Vehicle HAL | AIDL property poll + event subscribe | file / log
QNX / infotainment logs | logd + journald forwarder | file
ADAS events & camera | ROS 2 topics; clips captured on event | simulated
Diagnostic logs (DTC/UDS) | ISO-14229 listener, ring buffer | protocol
Retention tiers — real-time + historical
Hot: last 48 h in RAM/SQLite — live queries and fast path
Warm: 4–6 weeks in partitioned Parquet on eMMC/NVMe — trends & anomalies
Cold: zstd-compressed trip archives for forensics (months)
≈ 25–60 MB/day → ≤ 3.5 GB holds 60 days of history [Assumption → measured in Round 2]
Recreating driving scenarios & faults
CARLA + SUMO drive cycles (city, highway, cold morning)
Fault injection: DTCs, thermal derate, ADAS shadow events
Recorded CAN / ROS 2 logs replayed with can-utils player
6 ground-truth scenarios with golden questions and answers
Data maturity tags
protocol = live bus decode · file = parsed log · simulated = CARLA/replay. Every dashboard and answer carries its tag — no simulated data is presented as measured.
Time alignment
One monotonic clock across sources (PTP/NTP disciplined); every event carries a ±30 s context window so “what happened before” queries are exact.
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
4 / 10

## Slide 6
EXPECTED OUTPUT 3 · SLM / LLM SELECTION RATIONALE
Smallest model that clears the bar — quantised, permissive, CPU-first
Model | Params | Licence | RAM @ Q4_K_M | Verdict
Qwen2.5-1.5B-Instruct | 1.5B | Apache-2.0 | ≈ 1.0 GB | SELECTED — 32k context, strong function calling
Qwen2.5-0.5B-Instruct | 0.5B | Apache-2.0 | ≈ 0.4 GB | Fallback for the strict 2 GB configuration
Llama 3.2 1B Instruct | 1B | Llama Community | ≈ 0.8 GB | Comparison baseline in benchmarks
Phi-3.5-mini Instruct | 3.8B | MIT | ≈ 2.4 GB | Rejected — exceeds the 2 GB memory budget
Gemma 2 2B | 2B | Gemma Terms | ≈ 1.6 GB | Rejected — redistribution terms + budget
How the choice was made
Score = answer quality on a vehicle QA set × licence fit ÷ RAM cost; Apache-2.0 allows redistribution in the product
Runs CPU-only through llama.cpp (MIT) as 4-bit GGUF — no GPU/NPU dependency, deterministic packaging
Model role is deliberately narrow: classify the question, shape the answer from the evidence package, never compute figures
Grammar-constrained JSON output so the validator can parse, re-check and cite every claim
All RAM numbers are calculated estimates from declared assumptions → measured on the reference board [Design / Target]
Why a small model is enough
Numbers come from SQL/analytics, not from the LLM
SLM only does intent, summarisation and phrasing
4-bit weights: 0.4–1.0 GB → fits 2 GB with OS
Model file pre-loaded from disk — no network needed at boot
Guardrails on the model
Answer must cite evidence rows; no evidence → explicit “not found”
Refuses safety-adjacent advice; points to the manual/dealer
Model bundle swappable over-the-air without retraining
Upgradable tier (1.5B → 3B) on vehicle HPC
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
5 / 10

## Slide 7
EXPECTED OUTPUT 4 · SEARCH & RETRIEVAL WORKFLOW
Computed first, written second, verified always
Question
Intent router
Evidence engines
SLM composes
Validator + citations
FAST PATH — exact lookup
“when / show all / list” questions
Indexed temporal + DTC search, model skipped
Typically < 200 ms
ANALYTIC PATH — why / compare
SQL, trend and anomaly engines compute deltas
Ranks causal contributors with magnitudes
Returns rows, not prose
NARRATIVE PATH — what happened
Retrieval over event summaries + trip context
Small vector index over local embeddings
Feeds context window for the SLM
Worked example — end to end
Q: “Why has my driving range reduced over the last two weeks?”
Evidence: usable capacity −4.2% · mean consumption +9.8% · 3 cabin-preconditioning spikes on cold mornings · 1 tyre-pressure DTC — each with signal, value, timestamp
Answer: one-sentence cause + ranked contributors + trend chart + source chips; the validator re-derives every number or flags it
Latency: parse 50 ms · retrieve 300 ms · generate 900 ms · validate 150 ms ≈ 1.4 s [Target — measured in Round 2]
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
6 / 10

## Slide 8
EXPECTED OUTPUT 5 · HISTORICAL DATA STORAGE APPROACH
Weeks of searchable history in a few gigabytes — all on the vehicle
Tier | Store | Window | Serves
Hot | SQLite + in-process cache (WAL) | last 48 h | live queries, fast path, dashboards
Warm | Parquet + DuckDB, partitioned by day | 4–6 weeks | trends, anomalies, retrieval index
Cold | zstd-compressed trip archives | months | forensics, validation replay, export
Canonical schema (one model for every source)
signals(event_time, source, signal_id, value, unit, trip_id) — columnar, sorted for range scans
events(type, severity, source, window_start, window_end) — DTCs, ADAS disengagements, thermal warnings
trips(trip_id, scene, distance, energy, tags) — city / highway / cold-start labelling
notes(embedding, trip_id, text) — local embeddings for “what happened” semantic search
Written once by the ingest pipeline; read-only for the AI layer
Storage math
≈ 60 signals @ 10 Hz + events ≈ 25–60 MB/day
Delta + zstd compression ≈ 5–10×
≤ 3.5 GB holds 60 days on 16 GB eMMC
[Assumption → verified on reference board]
Search layer (all local)
DuckDB SQL over Parquet partitions
Inverted event index (DTC / signal keywords)
Small HNSW vector index for narrative search
Retention & privacy policy
Rolling window, auto-pruned — no cloud offload
Full wipe on owner/factory reset
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
7 / 10

## Slide 9
EXPECTED OUTPUT 6 · EDGE DEPLOYMENT ARCHITECTURE
One container image, four rungs — CI VM all the way to vehicle HPC
1
DEV / CI
x86 VM · CARLA + vCAN replay · QEMU / Cuttlefish — iterate freely at zero hardware cost
2
REFERENCE BOARD
Raspberry Pi 5 (4–8 GB) + AI HAT + NVMe — where the 2 GB / 2 s targets are proven
3
VEHICLE
Automotive-grade ARM SoC (Linux or QNX) · optional NPU · hypervisor-isolated AI partition
4
VEHICLE HPC
Same OCI image · larger model tier (1.5B → 3B) · multi-ECU fan-out, fleet-wide rollout
Packaging & operations
Single OCI container + systemd unit; signed OTA bundles for model, index and rules
Config selects model tier per hardware class; rollback on failed health check; safety partition never updated by this path
Component | 2 GB build | 4–8 GB build
SLM (Q4_K_M) | 0.4 GB (0.5B) | 1.0 GB (1.5B)
KV cache + runtime | 0.2 GB | 0.4 GB
DuckDB + indexes | 0.3 GB | 0.4 GB
Ingest + normalisers | 0.4 GB | 0.5 GB
OS + services | 0.6 GB | 1.0 GB
Total (target) | ≈ 1.9 GB | ≈ 3.3 GB
Latency budget [Target]
parse 50 ms · retrieve 300 ms · generate 900 ms · validate 150 ms ≈ 1.4 s end-to-end, inside the 2 s constraint.
Fast path keeps the promise
Exact lookups skip the model entirely — typically < 200 ms, leaving the budget for the hard “why” questions.
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
8 / 10

## Slide 10
EXPECTED OUTPUT 7 · USER INTERACTION · PRIVACY & SECURITY
Three modes, one answer contract, a hard safety boundary
DRIVER — head unit
Voice or typed question on the infotainment screen; short answer, trend sparkline, follow-up chips (“compare last month”, “what changed?”). No jargon, no raw signal names.
SERVICE ENGINEER — tablet
VIN-scoped session: DTC timeline, evidence rows, replay of the fault window; one tap exports the answer and its evidence into the repair order.
FLEET / VALIDATION — dashboard
Batch questions across vehicles, CSV/PDF export, scenario replay for regression runs — same engine, same citations.
Anatomy of an answer card
Claim (one sentence, plain language)
Evidence rows: signal · timestamp · value · delta
Trend chart + source chips; confidence and honesty labels ([Target], [Assumption])
Safety boundary — non-negotiable
Read-only taps: no CAN write, no actuator path
AI partition isolated by hypervisor + MMU; safety functions bypass the AI entirely
Privacy & security
Local-only processing: nothing leaves the vehicle
Role-based access, encrypted at rest, query audit log
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
9 / 10

## Slide 11
VALIDATION · ROADMAP · IMPACT
Targets we will measure — and the plan to hit them
Metric | Target | How it is measured
Query latency (common) | < 2 s | scripted 100-query set on the reference board
Fast-path lookup | < 200 ms | indexed temporal lookup benchmark
Memory footprint | ≤ 2 GB | cgroup telemetry during the query loop
Retrieval accuracy | ≥ 90% | 6 ground-truth scenarios, golden answers
Answer factuality | 100% validated | validator re-derives or flags every figure
History window | ≥ 4 weeks | retention test over a synthetic 60-day log
Honesty labels used throughout: [Official] from the case brief · [Design] our architecture choice · [Assumption] declared input · [Target] to be measured · [Future] beyond this round.
No measured results are claimed yet. Every performance figure in this deck is a design target or a calculated estimate; the Round 2 prototype fills the table with real numbers.
Roadmap to the Round 2 demo
M1 · Sim rig: CARLA + vCAN + ingest pipeline
M2 · Tiered store, SQL/temporal/anomaly search
M3 · SLM integration + evidence validator
M4 · Head-unit HMI, 2 GB / 2 s tuning, benchmark run
Demo: Pi 5 + AI HAT answering the 5 brief questions live
Innovation & practicality
Works offline in yards, workshops and tunnels
OTA-swappable model; plug-in normaliser per new source
Value: drivers get answers, engineers get evidence, fleets get trends, validation gets replay.
TELIPORT Season 4 | Case Study 5 - Natural Language Vehicle Information (VehicleGPT) | Team: <team name>
10 / 10